## Slide 1: Machine Learning techniques for automatic ocular artifact correction in resting state EEG Practices and recommendations for the CHDR
Lisa Tostrams, BSc (Radboud University)
Supervisors: Dr. J.D.R Farquhar (Radboud University) Dr. Y.M. Mejia (CHDR) Dr.ir. R.J. Doll (CHDR)

## Slide 2: Electroencephalography
One of the methods used by CHDR to assess the effect of a drug
Quantification of resting state EEG
Eyes closed, eyes open
Calculate power spectrum

## Slide 3: EEG and EOG
EEG often contains artefacts caused by EOG
Decreased the quality of the data and of the outcomes

## Slide 4: Ocular artefact correction
Two ways to deal with artefacts:
  Remove affected intervals
  Correct the signal
Research internship consisted of literary review
Methods for automated EOG correction

## Slide 5: Methods for ocular artefact correction
4 general classes:
  Linear regression
  Filtering
  Blind source separation
  Source decomposition
Requirements?
  Automated, correction not rejection, simplicity, quality..

## Slide 6: Methods and requirements
SOBI: Second order blind inference
Doesn’t require modelling, makes very few assumptions, relatively simple to implement

## Slide 7: Second Order Blind Inference
Blind source seperation: recover independent sources from signals that record a linear mixture
SOBI uses decorrelation across several lags as its basic computation
Resolved synchronized activity across time lags: important for propagating signals!

## Slide 8: Some results on simulated data
First column: simulated ‘true’ signal
Second column: simulated signal including artefacts
Third column: Signal corrected by SOBI

## Slide 9: Some results on acquired data

## Slide 10: How to validate?
Easy with simulated data: compare correction to true signal
  Signal to Noise Ratio
  Correlation increase
  Normalized Mean Squared Error
Harder with acquired data: quantitative evaluation of signal intervals with ocular artefacts
  Need a ground truth: signal labelled by domain expert
  Calculate true positives (corrects where artefact occurs)
  Calculate false positives (corrects when no artifacts occurs)

## Slide 11: What’s left to do?
Optimalization
  Current SOBI implementation takes a lot of time..
  Due to one specific operation: joint diagonalization
  Need to find a more efficient computation
Operationalization
Validation